TOWN  OF  WELLESLEY

PERAMBULATION OF BOUNDARY MARKERS

IN THE 21TH CENTURY

TOWN OF WELLESLEY ENGINEERING DIVISION

DEPARTMENT OF PUBLIC WORKS

PREPARED BY WILLIAM D. MILLETT, P.L.S. AUGUST 2011

UPDATED BY: GERARD BRUNO, S.I.T./E.I.T MAY 2016

CHAPTER 42  -  BOUNDARIES OF CITIES AND TOWNS

Section 2.  The boundary markers of every town shall be located, the marks thereon renewed, and the year located marked upon the face thereof which bears the letter of the town locating its boundary, once every five years, by at least two of the selectmen of the town or by two substitutes designated by them in writing. The marking shall be made with a paint or other suitable marking material.

The proceedings shall be recorded with the town clerk and the board of selectmen of the town in writing signed under penalty of perjury setting forth which boundary marks were located, and those which were not located. A copy of such records shall also be sent, by registered letter, to the town clerk and the board of selectmen of any contiguous town.

Section 4.  The selectmen of contiguous towns shall, at the joint and equal expense of such towns, erect permanent stone monuments at every angle of their respective boundary lines and wherever a highway crosses such lines, unless such monument, two feet high from the ground, already exists or unless such lines are bounded by the sea or by a permanent stream. The monuments shall be well set in the ground, at least four feet high from its surface, and shall have the initial letters of the respective names of such towns legibly cut thereon.

Section 6.  A selectman who refuses or neglects to perform any duty required of him by the two preceding sections shall forfeit twenty dollars.

| RECORD OF PERAMBULATIONS |
| --- |
| YEAR | NEWTON | NEEDHAM | DOVER | NATICK | WESTON |
| 2011 | X | X | X | X | X |
| 2016 | April 8th & 22nd | April 8th | April 8th & 15th | April 15th | April 22nd |

THE LINE BETWEEN WELLESLEY AND NEWTON

1. N-W-W The corner of Wellesley, Weston and Newton is marked by a square iron pin set into a boulder which 3 x 6 feet in section and about 5 feet above the bed of the river.  It is located just off the southerly end of a small island in the Charles River.  This rock is called “County Rock” It can be seen from the bridge at the Leo J. Martin Golf Course which is just behind Crestwood Drive.  Cannot see iron pin from shore line.     (A canoe will be required to access the rock in order to observe the iron pin and mark.)

2.  The line between Wellesley and Newton was designated by the acts of 1711 as the Charles River when Needham was established.

3.  N-N-W WM The corner of Wellesley, Newton and Needham is in the center of the Charles River and is unmarked.  The witness mark was a wooden post in the center of an old dam or gate across the mouth of the reservoir channel and was 150’ to the northwest of the actual corner along the Wellesley and Needham line.  This location is now under a modern wooden foot bridge and there is no longer any evidence of the dam or post.

THE LINE BETWEEN WELLESLEY AND NEEDHAM

1.  N-N-W WM The corner of Wellesley, Newton and Needham is in the center of the Charles River and is unmarked.  The witness mark was a wooden post in the center of an old dam or gate across the mouth of the reservoir channel and was 150’ to the northwest of the actual corner along the Wellesley and Needham line.  This location is now under a modern wooden foot bridge and there is no longer any evidence of the dam or post.

2.  N-W1.  This angle point is a granite post set in a drainage ditch.  It is about 70’ due south of a traffic controller box.  Historic records indicate that the corner was unmarked and a witness point, N-W1 WM, was set about 215 feet to the southwest on Reservoir Street.  At that time the actual corner was in a small pond called “The Reservoir”.  Due to the construction of Route 128, the witness point was destroyed and the reservoir was filled.  Reservoir Street no longer exists.  Mass. DPW set a new post in 1968 which is believed to be the actual corner.  Its location should be verified by GPS.  There is no MHD data sheet for this corner.

3.  Road Stone, Cedar Street.  South side of Cedar Street about 15’ back from road.  The short post is opposite the last Wellesley hydrant.

4.  Road Stone post, 323 Oakland Street.  About 15’ back from road, north side across from nursery.

5.  Road Stone, Wellesley Avenue at Hunnewell Street.  Northwest side of the street.  It presents as an unmarked stone bound 1’ high about 4’ back from a wooden retaining wall. The bound appears tilted.

6.  Line Stone, Wellesley Avenue water treatment plant.  A standard stone bound with drill hole about 8” high.  41’ southwest along town line from corner of pumping station.

7.  Road Stone, Brookside Road.  Post west side of road about 10’ back.

8.  Road Stone, Forest Street.  Post southwest side of road, a few feet back.

9.  Road Stone, Great Plain Avenue.  Post southwest side of road near the RDF driveway entrance.

10.  Road Stone,  Cartwright Road.  Post southwest side about 8’ behind pole #19.

11.  Road Stone, Grove Street.  Post east side of road.

12.  Road Stone, Post southwest side of Winding River Road. The post appears to be in concrete material.

13.  D-N-W WM  The corner of Wellesley, Needham and Dover is in the center of the Charles River.  The witness mark is a granite post about 300’ northeast along the Wellesley Needham line.  It can be accessed from the Town of Needham tree farm on Charles River Street and Winding River Road and is in woodlands to the west of the planted trees.

THE LINE BETWEEN WELLESLEY AND DOVER

1.  D-N-W WM  The corner of Wellesley, Needham and Dover is in the center of the Charles River.  The witness mark is a granite post about 300’ northeast along the Wellesley Needham line.  It can be accessed from the Town of Needham tree farm on Charles River Street and Winding River Road and is in woodlands to the west of the planted trees.

2.  The line between Wellesley and Dover was designated by the acts of 1711 as the Charles River when Needham was established.  This line actually cuts back across the Charles River isolating a section of Wellesley.

3.  D-N-W WM  The corner of Wellesley, Dover and Natick is an unmarked point in the center of the Charles River.  A witness marker is a stone post about 60 feet south of the corner along the Natick Dover line.  It is located in thick and thorny underbrush just off the south bank of the river about 40’ east of the bridge abutment for the old trolley line.  It may be accessed from the Town of Natick land just to the left of #35 Dover Road by following the path of the old trolley line about 600 feet north to the river. (Tree clippers are required to trim back the underbrush in order to access the witness marker.)

THE LINE BETWEEN WELLESLEY AND NATICK

1.  D-N-W WM  The corner of Wellesley, Dover and Natick is an unmarked point in the center of the Charles River.  The witness marker is a stone post about 60 feet south of the corner along the Natick Dover line.  It is located in thick and thorny underbrush just off the south bank of the river about 40’ east of the bridge abutment for the old trolley line.  It may be accessed from the Town of Natick land just to the left of #35 Dover Road by following the path of the old trolley line about 600 feet north to the river. (Tree clippers are required to trim back the underbrush in order to access the witness marker.)

2.  Road Stone, north side of Washington Street, granite post just off the edge of the road next to the stone wall. About 1’ above the ground.

3.  Line Stone, Hunnewell property in the wooded area about 35’-50’ off the bottom embankment of the Sudbury Aqueduct. The granite stone is approximately 8” above the ground near a large pine tree and on private property. It could not be verified if this is actually a Town boundary marker. Needs verification if this is an actual boundary marker.

4.  Line Stone, Palmer land at 110 Pond Road. The granite stone is approximately 12”-16” above the ground and is tilted.

5.  Road Stone, Central Street, north side.  Granite post is approximately 18’ just off shoulder and under trees.

6.  Road Stone, Bacon Street, a stone bound with drill hole just off road in front of wood stockade fence at #23 College Road.

7.  N-W 2.  This corner is an angle in the line between Wellesley and Natick.  It is marked by a stone post that is no longer visible as it is in the flowed part of Morse’s Pond.  It was reported in 1904 to have fallen over and is still likely to be below the water surface.

8.  Road Stone, Worcester Street (Route 9) north side.  There is no evidence of this point as the area has been extensively changed.  It was reported to be a MHD bound with USC&G disk set flush with ground identified as M9BNW.  It may just be paved over.   To be in compliance with Chapter 42, Section 4, a new stone should be erected, possibly on the south side.

9.  N-W 1 This is the northwest corner of the Town.  It is a granite post at the top of a small hill at the left rear corner of #1 Ingleside Road.

10.   N-W-W  The corner of Wellesley, Natick and Weston.  A granite post behind #111 Manor Avenue near the right rear corner of the property.

THE LINE BETWEEN WELLESLEY AND WESTON

1.  N-W-W  The corner of Wellesley, Natick and Weston.  A granite post behind #111 Manor Avenue near the right rear corner of the property.

2.  Road Stone, Weston Road, east side, a post visible from the road behind a stone wall just to the right of a Town of Weston hydrant.

3.  Line Stone, in Rocky Ledges parkland, a stone bound almost flush with ground, appears to be newer and is most likely just a lot corner for property in Weston.  Access is from Yarmouth Road about 1000’ along the trail.  Stone is about 100’ west of the Belkin property to the right of the trail as it turns back into Wellesley and opposite some large glacial boulders.

4.  Line Stone, post on property of #70 Greylock Road on hill to right and rear of house.  Top is broken off, but it is securely wired to a steel post.

5.  Road Stone, Cliff Road west side at the bend, several feet back from pavement.  Appears as a stone bound flush with the ground, may be a post broken off at ground level.

6.  Road Stone, Glen Road, east side across from Glenbrook Road.  Granite post on side of hill behind the cement concrete block wall and can be easily seen from street.

7.  Road Stone  -  A short granite post at the intersection of Ox Bow Road and Boulder Lane.  It is in a rhododendron bush at the left front of the property at 39 Ox Bow Road.

8.  N-W-W. The corner of Newton, Weston and Wellesley is marked by a square iron pin set into a boulder in the Charles River. This rock is called “County Rock” as it also demarcates the Norfolk / Suffolk county line. It is located just off the southerly end of a small island.  The rock but not the iron pin can be seen from the river bank at the Leo J. Martin Golf Course which is just behind Crestwood Drive. The rock appears to be undisturbed. (A canoe will be required to access the rock in order to observe the iron pin and mark.)